LTD «КУ-КУ»

Address: 238300, Kaliningrad region,

30 Bezymyannaya, Gur’yevsk, Russia

Sales Dept. +7-911-486-79-30;

+7-911-460-97-63

Internet: penopolistirol-39.ru

E-mail:    info@penopolistirol-39.ru

Sales proposal for purchasing a SRP-3220 "Maksi" machine for shape cutting foam polystyrene

SRP-3220 "Maksi" was developed as a version for manufacturing trim molding: skirting plate, thermal insulation for "shell" type pipes, parts of frontal finish, packaging, etc.

At all the models of SRP series machines, it is possible to install up to 6 cutting strings simultaneously to increase performance. 100 meters of nichrome is suplied in a delivery set. See the addendum for detailed specifications.

Price of the machine w/o accessory equipment amounts to  160,000.00 rubles.

Preparation of a 2D model cut file does not require special skills, only the basic knowledge of "Corel Draw" and abidance with the operating instructions and guidelines on usng the machine's software suffices.

We have developed kit of optional equipment to expand the capabilities of the machine:

- Turntable is designed for cutting solid models from model files generated in 3D Max, AutoCAD editors and others that support export into the STL format. Since 2010, a new turntable with gear transmission has been used. That ensures the most precise turning of blank thus ensuring a high quality of finished products.

Price 15 thous. rubles

- SRP-M "Master" - a kit of accessory equipment for cutting solids of revolution in one go. To manufacture a template, a nichrome wire bent around the article outline is used. The delivery set comprises a manual cutting torch of the "hot knife" type for smoothing products or work in a free style. See the addendum for detailed specifications.

Price 22 thous. rubles

- SRP-Ts "Tsirkul" - accessory equipment for cutting radial arcuated articles. The suite operates following the principles of an ordinary caliper allowing to manufacture products of up to 3 meters in radius.

Price 16 thous. rubles

Warranty period 12 months. During the whole service life, the customer is provided with service support.

The equipment is commercially produced and is available at the warehouse in Novosibirsk.

Shipment on 100% prepayment basis.

Equipment is delivered to regions to the warehouse  freight forwarder at the customer's expense or by other shipping company available in the regions of the vendor and the customer.

Addendum

- SRP-3220 "Maksi" machine specifications

  - The product ensures cutting polystyrene following a pre-set program (graphic images within the workspace) using a heated string.

  - The string is made of nickel-chromium alloy of 0.3 mm in diameter.

  - The string is heated by electric current with electronic adjustment of heating rate.

  - The heating level is adjustable within  0 to 80 c.u (recommended values)

  - The idle speed – within 0 to 40 mm/sec (recommended values).

  - Cutting speed – within 0 to 25 mm/sec (depending on the density, humidity, and the temperature of the material being cut).

  - Table turning rate – within 0 to 20 deg/ sec ( programmable).

  - Turntable diameter – 760mm.

  - Overall dimensions of the blank – 1100 х 1250 х 2200 mm (WхHхD)

  - Overall dimensions of the machine – 1800 х 2000 х 2800 mm (WхHхD)

  - Overall dimensions of the machine when dismantled – 2600 х 500 х 500 mm (WхHхD)

  - Power consumption – no more than 2000 W.

  - Connection - USB port.

- SRP-M "Master" machine specifications

  - The product comprises:

    - Adjustable current source (0-20 A) for heating cutting wires

    - Vertical and horizontal guides with clamping devices to fix and smoothly move cutting wires.

    - Insulators to fasten wires to the guides with feed wires.

    - Kit of cutting wires.

    - Manual cutting torch.

  - Material of cutting wires – nichrome of the X15H60 or X20H80 grades of 0.3 to 1.8 mm in diameter. (Recommended wire X20H80-1.0mm.)

  - Wires are heated by electric current with electronic adjustment of heating rate.

  - Admissibles ratios of diameter and length of the cutting wire:

| Wire diameter | Minimum length | Maximum length |
| --- | --- | --- |
| 0.3 mm | 10 mm | 300 mm |
| 0.5 mm | 20 mm | 500 mm |
| 0.8 mm | 30 mm | 800 mm |
| 1.0 mm | 40 mm | 1000 mm |
| 1,5 mm | 50 mm | 1500 mm |
| 1.8 mm | 60 mm | 1800 mm |

  - The turntable of SRP-32XX machine rotational velocity is preset by the control computer of the machine depending on the density of material, heating rate, and the diameter of the blank. Selectable based on experience.

  - Smooth vertical movement – 1100 mm.

  - Overall dimensions of the blank, max. – 1000 х 1000 х 1000 mm (WхHхD)

  - Power consumption – no more than 250 W.

- Consumables:

The cutting string is made of nickel-chromium alloy of 0.3 mm in diameter.  When fully charged, the strings are replaced once every two weeks. The delivery set comprises nichrome stock of 100m which is sufficient for 4 to 6 months of operation. To avoid breakoff of the string, strings need to be preliminarily replaced once every two weeks on average with the machine fully charged.

Our company ships nichrome of the three diameters:

| Diameter | Price, rub./meter |
| --- | --- |
| 0.3 | 3.5 |
| 1.0 | 120 |
| 1.8 | 168 |