LTD «КУ-КУ»

Address: 238300, Kaliningrad region,

30 Bezymyannaya, Gur’yevsk, Russia

Sales Dept. +7-911-486-79-30;

+7-911-460-97-63

Internet: penopolistirol-39.ru

E-mail:    info@penopolistirol-39.ru

Sales proposal for purchasing a SRP-3221 "Maksi Universal" machine for cutting foam polystyrene

SRP-3221 "Maksi Universal" was developed for cutting trim molding (skirting plate, parts of frontal finish,  thermal insulation for "shell" type pipes, packaging, etc.), manufacture of packaging, manufacture of left-in-place forms. Cutting is effected with heated string (nickel-chromium alloy of 0.3 mm in diameter.

The work space of the machine is  2200х1500х1100mm, which allows manufacturing articles of large format. Up to 6 cutting strings simultaneously can be intalled at the machine, which allows increasing performance when cutting articles of same type.

The program precision of movement of the tool amounts to 50 microns thus ensuring high cutting quality for both imported and domestic raw materials.

Price of the machine w/o accessory equipment amounts to  160 thous. rubles.

The delivery set comprises all what is required for assembly, tuning, and start-up of the machine, including the required tools, instruction manuals, user guides, and software for the computer control of the machine.

Computer is not part of the delivery set.

We have developed kit of optional equipment to expand the capabilities of the machine:

- Turntable – is designed for cutting solid models from model files generated in 3D Max, AutoCAD editors and others that support export into the STL format. Table diameter – 760mm.

Since 2010, a new turntable with gear transmission has been used. Gear transmission ensures the most precise turning of blank thus ensuring a high quality of finished products. The turning precision is 0.015 degree per motor step. Turning rate – 20 deg/sec.

Price 15 thous. rubles

- SRP-M "Master" - a kit of accessory equipment for cutting solids of revolution in one go. To manufacture a template, a nichrome wire bent around the article outline is used. The delivery set comprises a manual cutting torch of the "hot knife" type for smoothing products or work in a free style.

Price 22 thous. rubles

- SRP-Ts "Tsirkul" - accessory equipment for cutting radial arcuated articles. The suite operates following the principles of an ordinary caliper allowing to manufacture products of up to 3 meters in radius.

Price 16 thous. rubles

- SRP-D "Duplikator" - accessory equipment developed to increase performance while cutting bulky articles. Allows for simultaneous cutting up to 16 3D models or solids of revolution. Pluggable instead of the turntable.

Price 35 thous. rubles.

Prices shown less VAT. No VAT is provided.

Warranty period 12 months. During the whole service life, the customer is provided with service support.

The equipment is commercially produced and is available at the warehouse in Novosibirsk.

Shipment on 100% prepayment basis.

The equipment that we manufacture is produced on the grounds of a patent of the Russian Federation and has the Certificate of Compliance  C-RU.MM04.B.01283

Addendum

# SRP-3221 machine specifications

  - The product ensures cutting polystyrene following a pre-set program (graphic images within the workspace) using a heated string.

  - The string is made of nickel-chromium alloy of 0.3 mm in diameter.

  - The string is heated by electric current with electronic adjustment of heating rate.

  - The heating level is adjustable within  0 to 80 c.u (recommended values)

  - The idle speed – within 0 to 40 mm/sec (recommended values).

  - Cutting speed – within 0 to 25 mm/sec (depending on the density, humidity, and the temperature of the material being cut).

  - Table turning rate – up to 20 deg/sec.

  - Table dimensions for blank attachment – 2800 х 1700 mm.

  - Turntable diameter – 760mm.

  - Overall dimensions of the blank – 2200 х 1100 х 1500 mm (WхHхD)

  - Overall dimensions of the machine – 2900 х 2000 х 1900 mm (WхHхD)

  - Overall dimensions of the machine when dismantled – 2600 х 500 х 500 mm (WхHхD)

  - Power consumption – no more than 1500 W. (incl. incandescence – 1000W).

  - Connection - USB port.

SRP-3221 Package Features

In the packaged state, SRP-3221 machine with a turntable takes up 6 seats of overall weight 100kg.

1. 2.8х0.11х0.11m   - 12 kg (box)

2. 0.86х0.25х0.25m - 15 kg (box)

3. 0.47х0.36х0.17m - 10 kg (box)

4. 0.43х0.26х0.22m - 23 kg (box)

5. 0.36х0.21х0.21m - 15 kg (box)

6. 0.86х0.86х0.11m - 25 kg (box)

- SRP-M "Master" machine specifications

  - The product comprises:

    - Adjustable current source (0-20 A) for heating cutting wires

    - Vertical and horizontal guides with clamping devices to fix and smoothly move cutting wires.

    - Insulators to fasten wires to the guides with feed wires.

    - Kit of cutting wires.

    - Manual cutting torch.

  - Material of cutting wires – nichrome of the X15H60 or X20H80 grades of 0.3 to 1.8 mm in diameter. (Recommended wire X20H80-1.0mm.)

  - Wires are heated by electric current with electronic adjustment of heating rate.

  - Admissibles ratios of diameter and length of the cutting wire:

| Wire diameter | Minimum length | Maximum length |
| --- | --- | --- |
| 0.3 mm | 10 mm | 300 mm |
| 0.5 mm | 20 mm | 500 mm |
| 0.8 mm | 30 mm | 800 mm |
| 1.0 mm | 40 mm | 1000 mm |
| 1,5 mm | 50 mm | 1500 mm |
| 1.8 mm | 60 mm | 1800 mm |

  - The turntable of SRP-32XX machine rotational velocity is preset by the control computer of the machine depending on the density of material, heating rate, and the diameter of the blank. Selectable based on experience.

  - Smooth vertical movement – 1100 mm.

  - Overall dimensions of the blank, max. – 1000 х 1000 х 1000 mm (WхHхD)

  - Power consumption – no more than 250 W.

SRP-M "Master" Package Features

The packaged suite "Master" takes up 2 seats, weighs 15kg.

1. 1.4х0.05х0.05m  -  3 kg (box)

2. 0.39х0.16х0.24m - 12kg (box)

- SRP-Ts "Tsirkul" machine specifications

  - The product comprises:

    - Adjustable current source (0-20 A) for heating cutting wires

    - Guides to fix and smoothly move the cutting wires.

    - Insulators to fasten wires to the guides with feed wires.

    - Kit of cutting wires.

  - Material of cutting wires – nichrome wire X20H80-1.0-1.8mm

  - Wires are heated by electric current with electronic adjustment of heating rate.

  - Admissibles ratios of diameter and length of the cutting wire:

| Wire diameter | Minimum length | Maximum length |
| --- | --- | --- |
| 1.0 mm | 40 mm | 1000 mm |
| 1,5 mm | 50 mm | 1500 mm |
| 1.8 mm | 60 mm | 1800 mm |

  - Maximum movement radius 3 m

  - Power consumption – no more than 250 W.

- SRP-D "Duplikator" machine specifications:

4.1. SRP-D "Duplikator" ensures synchronous automatic turning of several blanks made of polystyrene by an angle pre-set in the machine control program (series SRP-32хх).

4.2. Number of axes – 16.

4.3. Distance between axes – 80 mm.

4.4. Number of blanks installed at a time – from 1 to 16 (depending on the dimensions of the blank).

4.5. Direction of the turn is opposite for odd and even axes of SRP-D "Duplikator".

4.6. Maximum turning rate – 10 deg/sec.

4.7. Overall dimensions – 1700 х 115 х 70 mm (w/o leads, w/o fasteners)

- Consumables:

The cutting string is made of nickel-chromium alloy of 0.3 mm in diameter.  When fully charged, the strings are replaced once every two weeks. The delivery set comprises nichrome stock of 100m which is sufficient for 4 to 6 months of operation. To avoid break-off of the string, strings need to be preliminarily replaced once every two weeks on average with the machine fully charged.

Our company ships nichrome of the three diameters:

| Diameter | Price, rub./meter |
| --- | --- |
| 0.3 mm | 3.5 |
| 1.0 mm | 120 |
| 1.8 kg | 168 |