LTD «КУ-КУ»

Address: 238300, Kaliningrad region,

30 Bezymyannaya, Gur’yevsk, Russia

Sales Dept. +7-911-486-79-30;

+7-911-460-97-63

Internet: penopolistirol-39.ru

E-mail:    info@penopolistirol-39.ru

Sales proposal for purchasing a SRP-3223 "Mini" machine for cutting foam polystyrene

SRP-3223 "Mini" was developed as a work tool for display workshops, advertising agencies, as well as for foundry engineering. Cutting is effected with heated string (nickel-chromium alloy of 0.3 mm in diameter. Average wire consumption – 100m/5-6 months.

One meter of nichrome price – 3.5 rub./m. (100m is shipped in the delivery set)

The delivery set comprises all what is required for assembly, tuning, and start-up of the machine, including 100 m stock of nichrome, incandescence transformer, control unit, all the required elements of the frame and movement system.

SRP-3223 "Mini" machine specifications

| String material | Nickel-chromium alloy of 0.3mm in diameter. |
| --- | --- |
| String warm-up | By electric current with electronic adjustment of heating rate |
| Cutting speed | adjustable within 0 to 25 mm/sec (recommended programmable values) depending on the density, humidity, and the temperature of the material being cut |
| Table turning rate | within 0 to 20 deg/sec (programmable) |
| Table dimensions for blank attachment | 1200х800мм |
| Turntable diameter | 760мм |
| Effective volume of blank | 700х700х700mm (WхHхD) |
| Overall dimensions of the machine | 1300 х1000 х 1000mm (WхHхD) |
| Power consumption | No more than 500W ((incl. incandescence – 100W) |
| Connection | USB - port |
| File format for 2D cutting | PLT (CorelDraw, AutoCAD, etc.) |
| File format for 3D cutting | STL (AutoCAD, SolidWork’s, 3D’s Max) |

Files for 2D cutting can be prepared in any graphic editor that supports exports of files into the PLT format (CorelDraw, AutoCAD, etc.).

Price of the machine w/o accessory equipment amounts to  140 thous. rubles.

We have developed kit of optional equipment to expand the capabilities of the machine:

- Turntable – is designed for cutting solid models from model files generated in 3D Max, AutoCAD editors and others that support export into the STL format. Table diameter – 760mm.

Since 2010, a new turntable with gear transmission has been used. Gear transmission ensures the most precise turning of blank thus ensuring a high quality of finished products. The turning precision is 0.015 degree per motor step. Turning rate – 20 deg/sec.

Price 15 thous. rubles

(Prices are stated less VAT since we are not VAT payers)

Warranty period 12 months. During the whole service life, the customer is provided with service support. Maintenance is effected at the manufacturer's premises in Novosibirsk.

Shipment is effected by the  freight forwarder or any other convenient to the customer within 5 business days after 100% of prepayment.