LTD «КУ-КУ»

Address: 238300, Kaliningrad region,

30 Bezymyannaya, Gur’yevsk, Russia

Sales Dept. +7-911-486-79-30;

+7-911-460-97-63

Internet: penopolistirol-39.ru

E-mail:    info@penopolistirol-39.ru

Sales proposal for purchasing a SRP-3462 "Relief" machine for applying coatings

When using architectural frontal decoration made of foam polystyrene, the issue of environmental protection of the products comes up first. Adequately protected product made of foam polystyrene is able to withstand many years and can be used as facades of buildings thus facilitating the process of manufacture and assemblage considerably.

SRP--3462 "Relief" was designed especially to apply reinforcement layer upon trim molding: made of foam polystyrene (foam plastic).

Any filler of good adhesion to foam plastic can be used for reinforcement. Tests have proven high quality of the coating. The machine ensures a uniform layer of filler throughout the product length.

The design of the machine assumes using input and output drawing blocks which reproduce the outline of the products upon which a protective coating needs to be applied. The output drawing block is slightly bigger, which favors to applying a uniform reinforcement layer.

Blocks for drawing products can be manufactured from metal or plexiglass (thickness at least 10mm).

Technical Specification

| Recommended coatings | elastic plaster covering |
| --- | --- |
| Blank feed rate | within 0 to 6 m/min. (adjustable) |
| Maximum cross-section of the blank | 650х350mm (WхH) |
| Length of the blank | is not limited |
| Number of clamping rollers | 9шт. |
| Volume of bin for plastering mix | 56 liters |
| Transporter closed loop belt | 2640х750х2мм |
| Overall dimensions of the machine | 3300х1100х1300mm (LхWхH) |
| Overall dimensions of the machine in package | 2400х1300х1000mm (LхWхH) |
| Net/gross weight of the machine | 200/260 kg |
| Power supply | 220V 50Hz. (Euro - standard |
| Power consumption | no more than 400 W. |
| Operation mode | continuous |

Price: 190,000.00 rub.

The machine is assembled and tuned by the customer following the attached instructions. When strictly necessary, a specialist may be dispatched at the customer's expense.

Video: http://www.youtube.com/watch?v=vDlMjJuoOvc&feature=player_detailpage

Warranty period 12 months. During the whole service life, the customer is provided with service support.

Equipment is delivered after 100% prepayment up to the warehouse of the freight forwarder at the customer's expense or by other shipping company available in the regions of the vendor and the customer.

Photos of SRP-3462 "Relief" machine

Looking forward to successful cooperation!